Common Characteristics of Tsunami Simulation Codes:

- Version of Shallow Water Equations solved

  - linear vs. non-linear

  - flux vs. velocity

- Solver – finite difference (vs. finite element)

  - Method – explicit vs. implicit

  - Schema – leap-frog vs. upwind/downwind

  - Spatial solution

    - placement – generally staggered

    - order of approximation – 1st, 2nd, etc.

  - Time solution

    - placement - maybe either staggered or not

    - order of approximation – 2nd, 3rd, etc.

  - Stability equation details

- Miscellaneous Properties

  - Propagation details

    - Method of connection for sub-grids

    - Allowable ratios of sub-grid sizes

    - Allowable coordinate systems

    - Configurable parameter switch (i.e. bottom friction)

  - Runup details

    - Moving boundary condition or fixed

COMCOT Details:

- Simulates both propagation and runup

- Nested multi-grid finite difference model

- Uses staggered grid placement in space

- Calculations for free surface and volume flux staggered in time

- Solves either linear or non-linear version of shallow-water equations

- For linear version, uses explicit leap-frog finite difference scheme

- For non-linear version, uses explicit leap-frog finite difference scheme, with an upwind scheme for the non-linear convective terms

- Scheme is 1st order in time and 2nd order in space

- Can use either spherical or Cartesian coordinates in each sub-region

- Allows any ratio of grid sizes between two adjacent sub-regions

- Applies a moving boundary method

- Equations are written and solved in terms of fluxes

- Allows runs either with or without bottom friction

- For non-linear, stability is sqrt(gh)*dt/dx < 1, or dt < dx/sqrt(gh)

Tsunami Details:

- Only simulates propagation

- Nested multi-grid finite difference model

- Uses staggered grid placement in space

- Calculations for free surface and velocity staggered in time

- Solves either linear or non-linear version of shallow-water equations

- For linear version, uses explicit upwind scheme

- For non-linear version, uses explicit upwind scheme

- Scheme is 1st order in time and 2nd order in space

- Uses spherical coordinates for all calculations

- Allows size ratios of 3 or 5 between two adjacent sub-regions

- Applies a static boundary condition (velocities are always zero at shoreline)

- Equations are written and solved in terms of velocities

- Allows runs either with or without bottom friction

- For non-linear, stability is sqrt(2gh)*dt/dx < 1, or dt < dx/sqrt(2gh)