Tsunami Computational Portal Models

Configuration & I/O Definitions

Draft v0.7

Tom Logan

10/06

1	Preface	5

1.1	Note on ‘grids’:	5

1.2	Notes on Nomenclature:	5

1.3	Shortcomings of Draft v0.7:	6

1.4	Updates from Draft 0.3 to Draft v0.4:	6

1.5	Updates from Draft v0.4 to v0.7	7

2	Configuration Parameters	8

2.1	General Parameters	8

2.1.1	Job_Id	8

2.1.2	User_Id	9

2.1.3	Model_Name	9

2.1.4	Number_of_Time_Steps	9

2.1.5	Length_of_Time_Step	9

2.1.6	Output_Frequency	9

2.1.7	End_Time	10

2.1.8	Number_of_Outputs	10

2.1.9	Global_Nonlinear_Switch	10

2.1.10	Global_Friction_Switch	10

2.1.11	Coef_of_Bottom_Friction	10

2.1.12	Global_Max_Refinement	11

2.1.13	Refinement_Frequency	11

2.1.14	Shallow_Depth	11

2.1.15	Wave_Tolerance	11

2.1.16	East_West_Cells	11

2.1.17	North_South_Cells	12

2.2	Grid Specific Parameters	13

2.2.1	Grid_Number	13

2.2.2	Parent	13

2.2.3	Name	14

2.2.4	Output_Name	15

2.2.5	Latitude_SW_Corner	15

2.2.6	Longitude_SW_Corner	15

2.2.7	Latitude_NE_Corner	15

2.2.8	Longitude_NE_Corner	15

2.2.9	East_West_Points (X length)	16

2.2.10	North_South_Points (Y length)	16

2.2.11	Spacing	16

2.2.12	Parent_Child_Spacing_Ratio	16

2.2.13	X_Start (in Parent)	16

2.2.14	X_End (in Parent)	16

2.2.15	Y_Start (in Parent)	17

2.2.16	Y_End (in Parent)	17

2.2.17	Coordinate_Switch	17

2.2.18	Nonlinear_Switch	17

2.2.19	Friction_Switch	17

2.2.20	Depth_File	18

2.2.21	Deformation_File	18

2.2.22	Bathy_Max_Refinement	18

3	Configuration Parameters for Initial Conditions	19

3.1	Initial_Wave_Source	19

3.2	Fault Configuration Parameters	19

3.2.1	Focal_Depth	20

3.2.2	Fault_Length	20

3.2.3	Fault_Width	20

3.2.4	Dislocation	20

3.2.5	Strike_Direction	21

3.2.6	Dip_Angle	21

3.2.7	Slip_Angle	21

3.2.8	Domain_Latitude	21

3.2.9	Domain_Longitude	21

3.2.10	Epicenter_Latitude	21

3.2.11	Epicenter_Longitude	22

4	Output Job Results (.desc)	23

4.1	Job Metadata	23

4.1.1	Job_Id	23

4.1.2	Model	23

4.1.3	Model_Version	23

4.1.4	Executable_Date	24

4.1.5	Host_Platform	24

4.2	Job Timing Information	24

4.2.1	Request_Date	24

4.2.2	Submission_Date	24

4.2.3	Start_Date	24

4.2.4	End_Date	24

4.2.5	Completion_Date	24

4.2.6	Job_Elapsed	24

4.2.7	CPU_Elapsed	24

4.3	Repeatable Descriptor Information	25

4.3.1	Lib	25

4.3.2	Series_Name	25

4.3.3	Series_Size_Raw	25

4.3.4	Series_Size_Zip	25

4.3.5	Slmax_Name	25

4.3.6	Slmax_Size	25

4.3.7	Deformation_Name	25

4.3.8	Deformation_Size	26

4.3.9	Error_Name	26

4.3.10	Error_Size	26

5	File Formats	27

5.1	Input Configuration File (.cfg)	27

5.2	Input Bathymetry/Topography Data (.dep)	28

5.3	Input Initial Surface Deformation (.def)	28

5.4	Output Selected Sea Level (.series)	28

5.5	Output Maximum Sea Level (.slmax)	28

5.6	Output Job Results (.desc)	29

APPENDIX A: Example Tsunami.cfg configuration file	30

APPENDIX B: Example Comcot.cfg configuration File	33

APPENDIX C: Example Tsunami_CLAW.cfg configuration file	36

APPENDIX D: Additional Parameters for UAF Tsunami	39

D.1	Configuration Parameters	39

D.1.1	General Parameters	39

D.1.1.1	Display_Frequency	39

D.1.1.2	Watch_Frequency	39

D.1.1.3	Constant_Depth	39

D.1.1.4	Input_Format	39

D.1.1.5	Output_Format	40

D.1.1.6	Save_Maximum	40

D.1.1.7	Save_Minimum	40

D.1.2	Grid Specific Watch Point Parameters	40

D.1.2.1	Watch_Point	40

D.1.2.2	WP_j	41

D.1.2.3	WP_k	41

D.1.2.4	WP_Param	41

D.1.3	Grid Specific Watch Line Parameters	41

D.1.3.1	Watch_Line	42

D.1.3.2	Start_j	42

D.1.3.3	Start_k	42

D.1.3.4	Line_Length	42

D.1.3.5	Line_Direction	43

D.1.3.6	Line_Sign	43

D.2	Parameters for Initial Conditions	43

D.2.1	File Configuration Parameters	43

D.2.2	Sine Wave Configuration Parameters	43

D.2.2.1	Sin_Wave_j1	44

D.2.2.2	Sin_Wave_j2	44

D.2.2.3	Sin_Wave_k1	44

D.2.2.4	Sin_Wave_k2	44

D.2.2.5	Sin_Wave_Amp	44

D.2.2.6	Sin_Wave_Period	44

APPENDIX E: Additional Parameters for COMCOT	45

E.1	General Parameters	45

E.1.1	Input_Format	45

E.1.2	Output_Format	45

E.1.3	Save_Maximum	45

E.1.4	Save_Minimum	45

E.2	General Parameters for Initial Conditions	46

E.2.1	File Configuration Parameters	46

E.2.2	Wave Configuration Parameters	46

E.2.2.1	Wave_Type	46

E.2.2.2	Wave_Incident_Direction	47

E.2.2.3	Wave_Time_to_Change_Boundary	47

E.2.2.4	Wave_Boundary_After_Wave	47

E.2.2.5	Wave_Angular_Frequency	47

E.2.2.6	Wave_Height	48

E.2.2.7	Wave_Depth	48

E.2.2.8	Oblique_i_Index	48

E.2.2.9	Oblique_j_Index	48

E.2.2.10	Oblique_Angle	48

E.2.2.11	Profile_Name	48

E.2.2.12	Profile_Length	49

# Preface

This document describes in detail the configuration parameters, initial conditions, output job results description, and file formats for the models selected for the Tsunami Portal Project.  This document includes three tsunami simulation codes – UAF Tsunami, developed by researchers at the University of Alaska Fairbanks; COMCOT, developed by researchers at Cornell University; and Tsunami CLAW, developed by researchers at the University of Washington.

Through the efforts of this project, using the specifications put forth in this document, all three of these simulation codes have been modified to provide consistent control parameters, input files, and output files.

## Note on ‘grids’:

In this document, a grid refers to a computational domain through which the tsunami wave will be propagated.  A grid must have a bathy/topo input file and an entry in the configuration file in order to be valid.  Optionally, a deformation input file(s) (UAF Tsunami – 1 for each grid; COMCOT – 1 for entire run; Tsunami CLAW – 1 for entire run) may also be specified.  Separate output files will be written for each grid included in the computation.

## Notes on Nomenclature:

In all of the tables and definitions in this document, the following data types are used:

- BIN 		refers to a binary value (either 0 or 1),

- INT 		refers to an integer value,

- REAL 		refers to a floating-point value,

- DATE-TIME 	refers to the date-time string [Zone]:YYYYMMDD:HH:MM:SS, where zone is the time zone code,

- STRING 	refers to a character string, and

- FILE 	refers to a character string surrounded by single quotes, i.e. all file names consist of character strings which must be enclosed in single quotes, e.g.: Deformation_File='ini_surface.dat'.

Throughout this document, keywords are given an associated origin that specifies which subsystem is responsible for generating the value for this keyword.  For the input configuration file the origins are:

- AUTO 	a fixed value is automatically generated by the web interface,

- CALC	a modifiable value is calculated by the web interface,

- IMPLICIT	value is generated by the web interface via interpreting user input, (e.g. a user selects a region of interest by a bounding rectangle – this implicitly determines the Lat, Lon, number of lines and samples, and, for a sub grid, positioning of this grid in its parent.

- USER 		value is supplied by the user to the web interface.

For the output descriptor file, the origins are:

- INPUT		value is taken directly from the input configuration file

- ARSC_Agent	value is determined from the system by the ARSC_Agent

- BATCH	value is extracted from batch file output by the ARSC_Agent

- MODEL 	data is generated directly by a tsunami model.

## Shortcomings of Draft v0.7:

This draft of the Tsunami Portal Models Configuration and I/O Definitions is incomplete.  At a minimum, the following need to be completed:

Section 2.1	Calculation of default values for Number_of_Time_Steps, Length_of_Time_Step, and Output_Frequency need to be detailed.  These formulas will come from the stability equations for the models and other constraints still TBD.

Section 3.2	The fault configuration parameters still need full descriptions, ranges, defaults, and granularities.  In looking at the paper by Mansinha and Smylie, it is not at all obvious to the author what these 11 parameters mean.  One of the modelers will have to write this description.

Section 5.4	Need to add description of the format of Tsunami CLAW output files.

Section 5.5	Need to add description of the format of Tsunami CLAW output files.

Other	-  Should add an example output .desc file as an appendix.

- Will likely add an appendix stating any additional parameters for the 	Tsunami CLAW model.

## Updates from Draft 0.3 to Draft v0.4:

This version includes many updates and additions to the previous.

- Only minimal changes that affect the other components of the prototype phase of the project have been made.  These are:

  - New Keyword: Grid Specific – Coordinate_Switch (2.2.15)

  - Changed Keyword: Fault Specific – old Length; new Fault_Length (3.2.2)

  - Changed Keyword: Fault Specific – old Width; new Fault_Width (3.2.3)

- For parameters Name and Output_Name, an inconsistency between types given in the definitions (string) and types used in the example configuration files (FILE or quoted string) was discovered.  The examples were changed to match the definition.

- The new origin type CALC was introduced (1.2, Table 1) to more accurately reflect the origin of certain keywords

- One major update was the definition of ranges, units, defaults, and granularities for all keywords save those listed in section 1.3 above.

- Two appendices, Additional Keywords for Tsunami and Additional Keywords for COMCOT, have been added.

  - The primary goal of these keywords is ensuring that all functionality available in each code was retained.

  - Users of COMCOT can still read deformation files as well as access all invocations of the wave maker, including time series input files.

  - Tsunami runs can still be configured to use Sine waves or initial deformation files, watch point and watch lines can be collected at configurable frequencies, and constant depth runs are still an option.

  - Both codes have been implemented with Input_Format and Output_Format switches that allow either ASCII or binary format files to be read and/or written.

  - Both codes have been implemented with Save_Maximum and Save_Minimum switches that allow the creation of sea level maximum (.slmax) and sea level minimum (.slmin) files to be toggled on or off.

## Updates from Draft v0.4 to v0.7

Once again, many updates and additions have been added since the last version of this document.

- The document was reviewed and edited by Cherri Pancake.  In addition to many wording and style changes, the following edits were made:

  - The code previously named Tsunami has been renamed UAF Tsunami to allow for the addition of Tsunami CLAW and other future codes

  - The term key words has been replaced with the term parameters

- The third model, Tsunami CLAW has been added resulting in many changes.  The following additional parameters have been added to accommodate the Tsunami CLAW model:

    - 2.1.5 End_Time

    - 2.1.6 Number_of_Outputs

    - 2.1.10 Global_Max_Refinement

    - 2.1.11 Refinement_Frequency

    - 2.1.12 Shallow_Depth

    - 2.1.13 Wave_Tolerance

    - 2.1.14 East_West_Cells

    - 2.1.15 North_South_Cells

    - 2.2.7 Latitude_NE_Corner

    - 2.2.8 Longitude_NE_Corner

    - 2.2.22 Bathy_Max_Refinement

- Two new parameters were added for all models:

  - User_Id :  This is the user ID of the requestor for this run.  Currently it is not used, but once the portal is in production, this will be the ARSC user account that is charged for model runs.  Thus, the portal User_Id must be identical to the ARSC user ID for the requestor.

  - Model_Name : For absolute clarity, a model name parameter was added as a requirement for all configuration files.

- The definition of the parameter Deformation_Name has been modified.  When the Initial_Wave_Source is FILE, this parameter names the input deformation file for the model run.  When the Initial_Wave_Source is FAULT, this parameter names the output surface deformation files used as initial conditions by the model run.  In addition, rather than a single deformation file being created by the fault model, one deformation file will be created for each grid when using both the UAF Tsunami and the COMCOT codes.

- Details of the grid specific watchline parameters for the UAF Tsunami model have been more fully defined and described.

# Configuration Parameters

A common format configuration file will drive each Tsunami simulation code.  The portal front-end creates this file and then sends it with a job request to the ARSC agent.  Parameters are divided into three logical classes.  The general parameters, given in section 2.1, include job metadata, configuration of job length and outputs, and global processing switches.  Section 2.2 defines the specific parameters for each computational grid.  The third class, defining the generation of an initial wave source, is detailed in Section 3.

## General Parameters

This section describes each of the general parameters that may appear in a tsunami portal configuration file.  These parameters are summarized in table 1.

| PARAMETER KEYWORD | TYPE | UNITS | ORIGIN | Required UAF Tsunami | Required COMCOT | Required Tsunami CLAW |
| --- | --- | --- | --- | --- | --- | --- |
| Job_Id | INT |  | AUTO | YES | YES | YES |
| User_Id | STRING |  | AUTO | YES | YES | YES |
| Model_Name | STRING |  | AUTO | YES | YES | YES |
| Number_of_Time_Steps | INT |  | CALC | YES | YES | NO |
| Length_of_Time_Step | REAL | Seconds | CALC | YES | YES | NO |
| Output_Frequency | INT | Time steps | CALC | YES | YES | NO |
| End_Time | INT | Seconds | CALC | NO | NO | YES |
| Number_of_Outputs | INT |  | CALC | NO | NO | YES |
| Global_Nonlinear_Switch | BIN | 1-on; 0–off | USER | YES | NO | NO |
| Global_Friction_Switch | BIN | 1-on; 0–off | USER | YES | NO | YES |
| Coef_of_Bottom_Friction | REAL |  | USER | Optional | Optional | Optional |
| Initial_Wave_Source* | STRING |  | USER | YES | YES | YES |
| Global_Max_Refinement | INT |  | IMPLICIT | NO | NO | YES |
| Refinement_Frequency | INT |  | USER | NO | NO | YES |
| Shallow_Depth | REAL | Meters | USER | NO | NO | YES |
| Wave_Tolerance | REAL | Meters | USER | NO | NO | YES |
| East_West_Cells | INT |  | AUTO | NO | NO | YES |
| North_South_Cells | INT |  | AUTO | NO | NO | YES |

* Details of this parameter is given in section 3 Configuration Parameters for Initial Conditions

Table 1:  Summary of General Parameters

### Job_Id

Definition: Portal supplied job identification number.  Will be used to distinguish between job initiation requests.

Required: Yes

Type: INT

Default: AUTO

Notes: Actual values are still TBD – suggest 6-digit number with leading zeros

### User_Id

Definition: Portal supplied user identification for requestor of this run.  This ID will be the user’s login name on both the portal front-end and their ARSC user ID.

Required: Yes

Type: String

Default: None

Notes:  Requirement is that ARSC user id is established first and then used by the portal as well.

### Model_Name

Definition: Portal supplied model name

Required: Yes

Type: String

Default: None

Notes:  Actual values should be one of  UAF_TSUNAMI, COMCOT, or TSUNAMI_CLAW depending on the model selected by the portal user.

### Number_of_Time_Steps

Definition: The total number of time steps to simulate.

Required: UAF Tsunami – Yes; COMCOT – Yes; Tsunami CLAW - No

Type: INT

Range: 5000 - 500000

Default: CALC

Granularity: 100

### Length_of_Time_Step

Definition: The simulated time that elapses between each step in a run.  Thus the total simulated time will be Number of Time Steps * Length of Time Step.

Required: UAF Tsunami – Yes; COMCOT – Yes; Tsunami CLAW - No

Type: REAL

Units: Seconds

Range: Must obey stability conditions

Default: CALC

Granularity: 0.05

### Output_Frequency

Definition: The frequency of output to the sea level files during a run.

Required: UAF Tsunami – Yes; COMCOT – Yes; Tsunami CLAW - No

Type: INT

Units: Time Steps

Range: 1 to Number of Time Steps + 1

Default: CALC

Notes:  For UAF Tsunami, if Output Frequency > Number of Time Steps, no output series files will be written.

### End_Time

Definition: The total amount of time to simulate.  For Tsunami CLAW, this parameter takes the place of Number_of_Time_Steps * Length_of_Time_Step. Required: UAF Tsunami – No; COMCOT – No; Tsunami CLAW - Yes

Type: REAL

Units: Seconds

Range: 50 - 180000

Default: CALC

Granularity: 1.0

### Number_of_Outputs

Definition: The total number of outputs to the sea level files during a run.  For Tsunami CLAW, this parameter replaces Output_Frequency.

Required: UAF Tsunami – No; COMCOT – No; Tsunami CLAW - Yes

Type: INT

Units:

Range: 1 to End_Time

Default: CALC

### Global_Nonlinear_Switch

Definition: Switch to determine if nonlinear terms will be used in the calculations for all grids in a run.

Required: UAF Tsunami – Yes; COMCOT – No; Tsunami CLAW - No

Type: BIN

Range: 0 (off) or 1 (on)

Default: 0 (off)

### Global_Friction_Switch

Definition: Switch to determine if friction terms will be used in the calculations for all grids in a run

Required: UAF Tsunami – Yes; COMCOT – No; Tsunami CLAW - Yes

Type: BIN

Range: 0 (off) or 1 (on)

Default: 0 (off)

### Coef_of_Bottom_Friction

Definition: Value to use for the coefficient of bottom friction

Required: Optional.  Required when either global or grid-specific friction is being calculated (i.e., if Global_Friction_Switch or any grid-specific Friction_Switch is YES)

Type: REAL

Range: 0.0001-0.0999

Default: UAF Tsunami – 0.013; COMCOT – 0.0033; Tsunami CLAW – 0.025

Granularity: 0.0001

### Global_Max_Refinement

Definition: The maximum adaptive mesh refinement level allowed in this calculation

Required: UAF Tsunami – No; COMCOT – No; Tsunami CLAW - Yes

Type: INT

Range: 2 to 4

Default: levels of bathymetry data + 1

### Refinement_Frequency

Definition: The frequency to check for re-gridding of adaptive meshes

Required: UAF Tsunami – No; COMCOT – No; Tsunami CLAW - Yes

Type: INT

Units: Time Steps

Range: 1 to 4

Default: 1

### Shallow_Depth

Definition: Defines areas that are considered to be ‘near-shore’ and, thus, eligible for adaptive grid refinement.

Required: UAF Tsunami – No; COMCOT – No; Tsunami CLAW - Yes

Type: REAL

Units: Meters

Range: 1 to 5000

Default: 1000

Granularity: 1

### Wave_Tolerance

Definition: Minimum wave height to flag for adaptive mesh refinement.

Required: UAF Tsunami – No; COMCOT – No; Tsunami CLAW - Yes

Type: REAL

Units: Meters

Range: 0.005 to 1.0

Default: 0.01

Granularity: 0.005

### East_West_Cells

Definition: The number of east-west cells in the coarsest computational domain

Required: UAF Tsunami – No; COMCOT – No; Tsunami CLAW - Yes

Type: INT

Default: Level 0 parent grid East_West_Points / 8

### North_South_Cells

Definition: The number of north-south cells in the coarsest computational domain

Required: UAF Tsunami – No; COMCOT – No; Tsunami CLAW - Yes

Type: INT

Default: Level 0 parent grid North_South_Points / 8

## Grid Specific Parameters

The parameters defined in this section define a single computational domain (grid).  Each of the required parameters herein must be included for each grid used in the simulation.  These parameters are summarized in table 2.

| PARAMETER | TYPE | UNITS | ORIGIN | Required UAF Tsunami | Required COMCOT | Required Tsunami CLAW |
| --- | --- | --- | --- | --- | --- | --- |
| Grid_Number | INT |  | AUTO | YES | YES | YES |
| Parent | INT |  | USER | YES | YES | NO |
| Name | STRING |  | USER | YES | YES | YES |
| Output_Name | STRING |  | AUTO | YES | YES | YES |
| Latitude_SW_Corner | REAL | Degrees | IMPLICIT | YES | YES | YES |
| Longitude_SW_Corner | REAL | Degrees | IMPLICIT | INFO | INFO | YES |
| Latitude_NE_Corner | REAL | Degrees | IMPLICIT | NO | NO | YES |
| Longitude_NE_Corner | REAL | Degrees | IMPLICIT | NO | NO | YES |
| East_West_Points | INT | Points | IMPLICIT | YES | YES | YES |
| North_South_Points | INT | Points | IMPLICIT | YES | YES | YES |
| Spacing | REAL | Arc seconds | AUTO | YES | YES | YES |
| Parent_Child_Spacing_Ratio | INT |  | AUTO | YES | YES | YES |
| X_Start | INT | Points | IMPLICIT | YES | YES | NO |
| X_End | INT | Points | IMPLICIT | YES | YES | NO |
| Y_Start | INT | Points | IMPLICIT | YES | YES | NO |
| Y_End | INT | Points | IMPLICIT | YES | YES | NO |
| Coordinate_Switch | BIN | 1-Cart; 0-Sph | USER | NO | YES | YES |
| Nonlinear_Switch | BIN | 1 – on; 0 – off | USER | NO | YES | NO |
| Friction_Switch | BIN | 1 – on; 0 – off | USER | NO | YES | NO |
| Depth_File | FILE |  | AUTO | YES | YES | YES |
| Deformation_File | FILE |  | USER | Optional | Optional | Optional |
| Bathy_Max_Refinement | INT |  | USER | NO | NO | YES |

Table 2:  Summary of Grid Specific Parameters

### Grid_Number

Definition: Number of this grid, sequentially from 1.  This field is used to determine the nesting/connectivity of the grid domains (see parent).

Required: Yes

Type: INT

Range: 1 - 9

Default: AUTO

### Parent

Definition: Parent of this grid, i.e. the number of the grid that this grid is nested directly inside of.  Note that grid #1, and only grid #1, should have Parent=0.

Required: UAF Tsunami – Yes; COMCOT – Yes; Tsunami CLAW - No

Type: INT

Range: 0 for grid #1 only; otherwise 1 to the total number of grids

Default: Previous Grid_Number

Notes:  Connectivity of grids is specified using the Parent field in conjunction with the Grid_Number.  Grid #1 is always the topmost layer; it has Parent=0.  Grid #2 must be nested into grid #1, so it has Parent=1.  Grid #3 may be nested in Grid #1, in which case it has Parent=1, or it may be nested into grid #2, in which case it will have Parent=2, and so on for all other grids specified.  Currently, this hierarchy is limited to 1 topmost layer with four grids nested into the second layer, each of which may contain a single nested grid beneath.  Thus, a maximum of 9 grids may be used with a total nesting depth of 3.  See figure 1 for an example grid nesting.

Note on Tsunami CLAW:  Tsunami CLAW does not require special information regarding the nesting of grids in a run.  The only requirement is that the first grid specified covers the entire computational domain.

Grid_Number=1; Parent=0

Grid_Number=6

Grid_Number=2					Parent=1

Parent=1							Grid_Number=7

Grid_Number=3				Parent=6

Parent=1

Grid_Number=4

Parent=2		    Grid_Number=5			Grid_Number=8

Parent=3			Parent=1

Grid_Number=9

Parent=8

Figure 1:  Example Grid Nesting

This example shows the maximum allowable number of grids and grid nesting.  One topmost grid (#1) may contain up to 4 sub-grids (#2, #3, #6, #8), each of which may contain a single sub-grid (#4, #5, #7, #9).  Note that a grid’s parent may be any previously defined grid, not just the grid defined sequentially before it.

### Name

Definition: The given name of this grid domain.  Useful for remembering where each grid is located

Required: Yes

Type: STRING

Default: Grid<Grid_Number>

### Output_Name

Definition: The base name of the output files written for this grid.  This value is created by concatenating the names of each grid this grid is nested inside of.  That is, for the topmost grid, Output_Name=<Name>.  Each 2nd level grid will have Output_Name=<Topmost grid Name>.<this grid Name>.  Each 3rd level grid will have Output_Name=<Topmost grid Name>.<Parent’s Name>.<this grid Name>.  For examples, see the configuration files in Appendix A and Appendix B.

Required: Yes

Type: STRING

Default: AUTO

### Latitude_SW_Corner

Definition: Latitude for the southwest corner of this grid

Required: Yes

Type: REAL

Units: degrees

Range: -90 to +90

Default: IMPLICIT

Granularity: 0.000001

### Longitude_SW_Corner

Definition: Longitude of the southwest corner of this grid

Required: Yes

Type: REAL

Units: degrees

Range: -180 to +180

Default: IMPLICIT

Granularity: 0.000001

### Latitude_NE_Corner

Definition: Latitude for the northeast corner of this grid

Required: UAF Tsunami – No; COMCOT – No; Tsunami CLAW - Yes

Type: REAL

Units: degrees

Range: -90 to +90

Default: IMPLICIT

Granularity: 0.000001

### Longitude_NE_Corner

Definition: Longitude of the northeast corner of this grid

Required: UAF Tsunami – No; COMCOT – No; Tsunami CLAW - Yes

Type: REAL

Units: degrees

Range: -180 to +180

Default: IMPLICIT

Granularity: 0.000001

### East_West_Points (X length)

Definition: Total number of points in the east-west direction.

Required: Yes

Type: INT

Units: points

Range: 50 - 5000

Default: IMPLICIT

### North_South_Points (Y length)

Definition: Total number of points in the north-south direction.

Required: Yes

Type: INT

Units: points

Range: 50 - 5000

Default: IMPLICIT

### Spacing

Definition: Distance between each point in the grid.

Required: Yes

Type: REAL

Units: arc seconds

Default: AUTO

### Parent_Child_Spacing_Ratio

Definition: Ratio of grid spacing between parent and child.

Required: Yes

Type: INT

Range: UAF Tsunami – 3 or 5; COMCOT – 2 or larger; Tsunami CLAW - any

Default: AUTO

Notes:  This parameter is not used for grid 1.

### X_Start (in Parent)

Definition: Starting X-position of this grid in its parent grid

Required: UAF Tsunami – Yes; COMCOT – Yes; Tsunami CLAW - No

Type: INT

Units: points

Range: 2 to (X length –2) of parent grid

Default: IMPLICIT

Notes:  This parameter is not used for grid 1.

### X_End (in Parent)

Definition: Ending X-position of this grid in its parent grid

Required: UAF Tsunami – Yes; COMCOT – Yes; Tsunami CLAW - No

Type: INT

Units: points

Range: (X Start+1) to (X length-1) of parent grid

Default: IMPLICIT

Notes:  This parameter is not used for grid 1.

### Y_Start (in Parent)

Definition: Starting Y-position of this grid in its parent grid

Required: UAF Tsunami – Yes; COMCOT – Yes; Tsunami CLAW - No

Type: INT

Units: points

Range: 2 to (Y length –2) of parent grid

Default: IMPLICIT

Notes:  This parameter is not used for grid 1.

### Y_End (in Parent)

Definition: Ending Y-position of this grid in its parent grid

Required: UAF Tsunami – Yes; COMCOT – Yes; Tsunami CLAW - No

Type: INT

Units: points

Range: (Y Start+1) to (Y length-1) of parent grid

Default: IMPLICIT

Notes:  This parameter is not used for grid 1.

### Coordinate_Switch

Definition: Switch to determine the coordinate system for this grid.

Required: UAF Tsunami – NO; COMCOT – Yes; Tsunami CLAW - Yes

Type: BIN

Range: 0 – Spherical coordinates are used.  1 – Cartesian coordinates are used. Default: 0

Notes:  Currently, this switch may only have a value of 0 for the portal project.

### Nonlinear_Switch

Definition: Switch to determine if nonlinear terms will be used in the calculations for this grid.

Required: UAF Tsunami – No; COMCOT – Yes; Tsunami CLAW - No

Type: BIN

Range: 0 (off) or 1 (on)

Default: 0 (off)

### Friction_Switch

Definition: Switch to determine if friction terms will be used in the calculations for this grid.

Required: UAF Tsunami – No; COMCOT – Yes; Tsunami CLAW - No

Type: BIN

Range: 0 (off) or 1 (on)

Default: 0 (off)

Notes: For COMCOT, this switch is only available when using Cartesian coordinates with the nonlinear terms on.  Thus, it will not be a valid option for the first phase of the portal project.

### Depth_File

Definition: Name of the input topo/bathy file for this grid.

Required: Yes

Type: FILE

Default: Grid_Name.dep

### Deformation_File

Definition: This parameter has two purposes.  First, it is the name of the input initial surface deformation file for this grid whenever the Initial_Wave_Source is FILE.  Alternately, it is the name of output surface deformation file whenever the Initial_Wave_Source is FAULT.

Required: Required whenever Initial_Wave_Source is FILE or FAULT.  In either case, it will be required for each grid specified in the simulation.

Type: FILE

Default: Grid_Name.def

### Bathy_Max_Refinement

Definition: Maximum level of adaptive mesh refinement allowed for this grid.

Required: UAF Tsunami – No; COMCOT – No; Tsunami CLAW - Yes

Type: INT

Range: 2 to Global_Max_Refinement

Default: Grid level + 1 (topmost grid is level 1)

# Configuration Parameters for Initial Conditions

Once the computational grids in suitable bathy/topo regions have been populated, the next step is to specify an initial wave source to generate the tsunami. For this proof of concept phase of the project, the only allowable initial conditions will be via fault model generation of initial surface deformation files. In the future, configuration files will allow selection of earthquake faults, sinusoidal or soliton wave generation, user supplied initial surface deformation files, and land slide/bottom displacement models.

## Initial_Wave_Source

The keyword used to select different initial conditions is Initial_Wave_Source.

Initial_Wave_Source:

Definition: Switch to determine the wave source for this simulation.

Required: Yes

Type: STRING

Range: FAULT | FILE | WAVE,

Default: FAULT

Notes: Initially, only the value of FAULT will be supported.  Other options will be added in the future.

For each initial wave source option, an additional set of parameters will need to be populated.  The parameters common to both models are detailed in the remainder of this section; those specific to either of the models appear in Appendices C (UAF Tsunami) and D (COMCOT).

Basically, specification of Initial_Wave_Source=FAULT requires the series of generic parameters listed in this section.  Use of Initial_Wave_Source=FILE requires the model-specific parameters describing the format of the user-supplied file detailed in Section 1.1 of the appendix (D or E) corresponding to the particular model, while  Initial_Wave_Source=WAVE requires the model-specific parameters described in Section 2 of the same appendix.

## Fault Configuration Parameters

When the value of FAULT is used for Initial_Wave_Source, the displacement of the sea floor is determined from a linear elastic dislocation theory by Mansinha and Smylie.  In this case, the 11 sub-parameters for a specific earthquake, given in table 3 below, have to be defined in the configuration file.  The ARSC preprocessing subsystem will then be responsible for generation of the initial surface deformation files using these parameters.

| TYPE | PARAMETER KEYWORD | TYPE | UNITS | ORIGIN |
| --- | --- | --- | --- | --- |
| FAULT | Focal_Depth | REAL | Meters | USER |
|  | Fault_Length | REAL | Meters | USER |
|  | Fault_Width | REAL | Meters | USER |
|  | Dislocation | REAL | Meters | USER |
|  | Strike_Direction | REAL | Degrees | USER |
|  | Dip_Angle | REAL | Degrees | USER |
|  | Slip_Angle | REAL | Degrees | USER |
|  | Domain_Latitude | REAL | Degrees | AUTO |
|  | Domain_Longitude | REAL | Degrees | AUTO |
|  | Epicenter_Latitude | REAL | Degrees | USER |
|  | Epicenter_Longitude | REAL | Degrees | USER |

Table 3:  Summary of Fault Generation Parameters

### Focal_Depth

Definition: Focal depth of the source earthquake

Required: Yes

Type: Real

Units: meters

Range:

Default:

Granularity:

### Fault_Length

Definition: Length of the source earthquake

Required: Yes

Type: Real

Units: meters

Range:

Default:

Granularity:

### Fault_Width

Definition: Width of the source earthquake

Required: Yes

Type: Real

Units: meters

Range:

Default:

Granularity:

### Dislocation

Definition: Dislocation of the source earthquake

Required: Yes

Type: Real

Units: meters

Range:

Default:

Granularity:

### Strike_Direction

Definition: Strike direction of the source earthquake

Required: Yes

Type: Real

Units: degrees

Range:

Default:

Granularity:

### Dip_Angle

Definition: Dip angle of the source earthquake

Required: Yes

Type: Real

Units: degrees

Range:

Default:

Granularity:

### Slip_Angle

Definition: Slip angle of the source earthquake

Required: Yes

Type: Real

Units: degrees

Range:

Default:

Granularity:

### Domain_Latitude

Definition: Latitude at origin of computational domain

Required: Yes

Type: Real

Units: degrees

Default: AUTO

### Domain_Longitude

Definition: Longitude at origin of computational domain

Required: Yes

Type: Real

Units: degrees

Default: AUTO

### Epicenter_Latitude

Definition: Latitude of the epicenter

Required: Yes

Type: Real

Units: degrees

Range: -90 to +90

Default: CALC

Granularity: 0.000001

### Epicenter_Longitude

Definition: Longitude of the epicenter

Required: Yes

Type: Real

Units: degrees

Range: -180 to +180

Default: CALC

Granularity: 0.000001

# Output Job Results (.desc)

The output job results file contains information and statistics from a model run.  It has the same ‘keyword=value’ format as the input configuration file, with the parameters given in table 4 recording the pertinent metadata for this run.

| PARAMETER | TYPE | UNITS | ORIGIN | NOTES |
| --- | --- | --- | --- | --- |
| Job_Id | INT |  | INPUT | Given job id for portal run |
| Model | STRING |  | INPUT | Name of the model that ran |
| Model_Version | STRING |  | MODEL | Source code version of model |
| Executable_Date | DATE-TIME |  | AGENT | Executable date for model |
| Host_Platform | STRING |  | AGENT | Name of platform model ran on |
| Request_Date | DATE-TIME |  | INPUT | portal job requested |
| Submission_Date | DATE-TIME |  | BATCH | batch job submitted |
| Start_Date | DATE-TIME |  | BATCH | batch job started execution |
| End_Date | DATE-TIME |  | BATCH | batch job completed execution |
| Completion_Date | DATE-TIME |  | AGENT | portal job completed |
| Job_Elapsed | REAL | Sec | AGENT | Total elapsed time for job |
| CPU_Elapsed | REAL | Sec | BATCH | CPU elapsed time for model |
| Lib | STRING |  | MODEL | Name & Version of library used by model |
| Series_Name | STRING |  | AGENT | Name of time series data file |
| Series_Size_Raw | INT | Kbytes | AGENT | Size of time series file uncompressed |
| Series_Size_Zip | INT | Kbytes | AGENT | Size of time series file compressed |
| Slmax_Name | STRING |  | AGENT | Name of sea level maximum file |
| Slmax_Size | INT | Kbytes | AGENT | Size of slmax file |
| Deformation_Name | STRING |  | AGENT | Name of surface deformation file |
| Deformation_Size | INT | Kbytes | AGENT | Size of surface deformation file |
| Error_Name | STRING |  | AGENT | Name of error file |
| Error_Size | INT | Kbytes | AGENT | Size of error file |

Table 4:  Output Job Results Parameters

This table lists all of the output job results parameters.  Italics denote repeatable groups of parameters.  See section 3.6.3 for details.

## Job Metadata

The job metadata parameters report the job id and model related information.

### Job_Id

Definition: Job identification for this portal run.

Notes: This field will be a copy of the Job_Id given in the configuration file.

### Model

Definition: Name of the tsunami model used for this run.

Notes:

### Model_Version

Definition: Version of the model that was executed.

Notes: Taken from the output of the batch submission.  Each code will have to display its version number at the outset of the run.

### Executable_Date

Definition: Compilation Date-Time string for the executable used for this run.

Notes:  This value will be taken from a system call made either by the finalization agent or by the batch script.

### Host_Platform

Definition: Name of the host platform.

Notes:  Exact content of this field TBD.

## Job Timing Information

The job timing parameters contain information on the start, progress, and completion of a job.  All _Date parameters are of the type Date-Time, which includes the date and time to the nearest second.  The _Elapsed parameters take on real values in units of seconds.

### Request_Date

Definition: Date the job initiation request was received.

### Submission_Date

Definition: Date the batch job was submitted.

### Start_Date

Definition: Date the model run started execution.

### End_Date

Definition: Date the model run completed execution.

### Completion_Date

Definition: Date the job finalization completed.

Notes:  This value will not be entirely accurate as the .desc file will have to be written (containing this word) prior to full completion of the job.  To minimize this discrepancy, this value will be populated near the final processing step.

### Job_Elapsed

Definition: Elapsed time from the request date to the completion date.

### CPU_Elapsed

Definition: Elapsed CPU time for this job.

Notes: This value will be taken from the batch submission script output file.  Each batch job will track and report elapsed CPU.

## Repeatable Descriptor Information

The repeatable descriptor parameters take on values describing the libraries used for the run and the output file names and sizes.  These parameters may only occur in related groups of values, as denoted by the borders in table 5.  For each instance of a group, all keys in the group must be specified.  A job results file may contain one or more occurrences of the series and slmax parameter groups, and zero or more occurrences of the lib, deformation, and error parameter groups.

### Lib

Definition: Name and version of the library called by a model.

Notes: This is an optional parameter that may appear zero or more times.

### Series_Name

Definition: Name of the time series file created by the job.

Notes: This parameter will be repeated once for each grid specified in the job.  It will always appear immediately before parameters Series_Size_Raw and Series_Size_Zip.

### Series_Size_Raw

Definition: Size of the time series file created by this job, given in Kilobytes.

Notes: This parameter will be repeated once for each grid specified in the job.  It will only appear between the corresponding Series_Name and Series_Size_Zip parameters.

### Series_Size_Zip

Definition: Size of the compressed time series file, given in Kilobytes.

Notes: This parameter will be repeated once for each grid specified in the job.  It will only appear after the corresponding Series_Name and Series_Size_Raw parameters.

### Slmax_Name

Definition: Name of the sea level maximum file created by this job.

Notes: This parameter will be repeated once for each grid specified in the job in conjunction with the parameter Slmax_Size.

### Slmax_Size

Definition: Size of the sea level maximum file, given in Kilobytes

Notes: This parameter will be repeated once for each grid specified in the job in conjunction with the parameter Slmax_Name.

### Deformation_Name

Definition: Name of the surface deformation file created by this job.

Notes: For all runs that have Initial_Wave_Source=FAULT, this parameter will occur and be repeated once for each grid specified in the job.  It will always occur immediately prior to the corresponding Deformation_Size parameter.

### Deformation_Size

Definition: Size of the deformation file, given in Kilobytes

Notes: This parameter will be repeated once for each occurrence of the Deformation_Name parameter.

### Error_Name

Definition: Name of error file created by this job.

Notes: At this time, the format and content of the error files is TBD.  One possibility is that the batch script error file maybe included in the outputs.  Other files may be included in the future.  Thus, this parameter may occur zero or more times in conjunction with the Error_Size parameter.

### Error_Size

Definition: Size of the deformation file, given in Kilobytes

Notes: This parameter will be repeated once for each occurrence of the Error_Name parameter.

# File Formats

Both binary and ASCII data files will be passed by the portal<->ARSC_agent interface.

First, the portal will create an ASCII input configuration file named Tsunami.cfg, Comcot.cfg, or Tsunami_CLAW.cfg for UAF Tsunami, COMCOT, or Tsunami CLAW runs, respectively.  Next, it will create one binary format bathy/topo data file for each grid specified by the user.  These will be named <Grid_Name>.dep (for water depth).  The portal then transfers these files to the ARSC agent via a job initiation request.  During preprocessing, the ARSC agent may create optional input binary files describing the initial surface deformation for each grid in this run.  If these files are created, they will be named <Grid_Name>.def (for surface deformation).  For each grid, the model run will create two binary output files.  The will be given the base name <Output_Name> and extensions of .series for time series data and .slmax for sea level maximum.  Finally, the ARSC agent will summarize the job results in an ASCII file named Tsunami.desc, Comcot.desc, or Tsunami_CLAW.desc for UAF Tsunami, COMCOT, or Tsunami CLAW jobs, respectively.  These naming convention are summarized in table 5.

| Input File Names | Format | Contents | Created By |
| --- | --- | --- | --- |
| Tsunami.cfg | ASCII | UAF Tsunami configuration | Portal |
| Comcot.cfg | ASCII | COMCOT configuration | Portal |
| Tsunami_CLAW.cfg | ASCII | Tsunami CLAW configuration | Portal |
| <Grid_Name>.dep | BINARY | Bathy/Topo Data | Portal |
| <Grid_Name>.def | BINARY | Initial Surface Deformation | ARSC_Agent |
| Output File Names |  |  |  |
| <Output_Name>.series | BINARY | Time series | Model |
| <Output_Name>.slmax | BINARY | Sea level maximum | Model |
| Tsunami.desc | ASCII | UAF Tsunami Model Job summary | ARSC_Agent |
| Comcot.desc | ASCII | COMCOT Model Job summary | ARSC_Agent |
| Tsunami_CLAW.desc | ASCII | Tsunami CLAW Model Job Summary | ARSC_Agent |

Table 5:  File Naming Conventions

This table lists input and output file naming conventions for the project.  Note that the input configuration files have hard coded names Tsunami.cfg, Comcot.cfg, or Tsunami_CLAW.cfg.  All other names include user specified identifiers.

## Input Configuration File (.cfg)

The tsunami portal configuration file will contain all required general parameters, one or more sets of required grid specific parameters, and, optionally, a set of initial wave generation parameters. The configuration file name is hard coded to ’Tsunami.cfg’ for the UAF Tsunami code, ‘Comcot.cfg’ for COMCOT, and ‘Tsunami_CLAW.cfg’ for Tsunami CLAW. Please see appendix A for an example Tsunami.cfg file, appendix B for an example Comcot.cfg file, and appendix C for an example Tsunami_CLAW.cfg file.

Each line in the configuration file must start with either a keyword or a # sign with the exception that leading spaces and blank lines are ignored.  The # sign denotes a comment line which will be ignored.  Parameter declarations are of the form ‘keyword=value’, where keyword is a single parameter name and value is of the type specified for the parameter.  There can be no spaces either before or after the ‘=’ in any of these entries.  All keywords are case sensitive.

To distinguish between grids, all grid specific parameters between the statement Grid_Number=N and Grid_Number=N+1 are assigned to grid N.

## Input Bathymetry/Topography Data (.dep)

For each grid, the portal must provide a combined bathymetry/topography data file.  This file contains ocean bottom depth as well as land elevation information.  It contains positive floating-point values for increasing water depth and negative decreasing values for increasing land elevations.  The data is given in units of meters.  The file is organized from west to east (samples) and south to north (lines), written in IEEE 4-byte floating-point binary format, with East_West_Points by North_South_Points values.  For the UAF Tsunami and COMCOT codes, the following conditions must hold for each nested grid:

East_West_Points = (X_End-X_Start+1)*Parent_Child_Spacing_Ratio

North_South_Points = (Y_End-Y_Start+1)*Parent_Child_Spacing_Ratio

## Input Initial Surface Deformation (.def)

The input deformation file describes mean sea level deformation.  It contains both positive (crest) and negative (trough) floating-point values that have been derived from some surface deformation model.  The data is given in units of centimeters.  The file is organized from west to east (samples) and south to north (lines), written in IEEE 4-byte floating-point binary format, with East_West_Points by North_South_Points values.  These files are optional (required only if the user has chosen FILE as the value for Initial_Wave_Source.  If selected, they will be created by the ARSC agent, used for the run, and then returned to the portal with the other results.

## Output Selected Sea Level (.series)

The sea level series files record a time series of sea level values from a model run.  One series file, named <Output_Name>.series, will be created for each grid.

For COMCOT and the UAF Tsunami codes, each file contains a set of frames of size EAST_WEST_POINTS * NORTH_SOUTH_POINTS values taken at the interval given by the Output_Frequency parameter of the configuration file.

The output file format for Tsunami CLAW varies and will not be described in this version of the document.

## Output Maximum Sea Level (.slmax)

Maximum sea level files record the maximum sea level over the entire simulation.  The maximum is tracked for every cell of every grid for each iteration.  One sea level maximum file, named <Output_Name>.slmax, will be created for each grid.

For COMCOT and the UAF Tsunami codes, each file contains EAST_WEST_POINTS * NORTH_SOUTH_POINTS values.

The output file format for Tsunami CLAW varies and will not be described in this version of the document.

## Output Job Results (.desc)

The output job results file contains information and statistics from a model run.  It has the same format as the input configuration file.  It contains the job results parameters and their corresponding values.

# APPENDIX A: Example Tsunami.cfg configuration file

This appendix contains an example Tsunami.cfg file.

The global information specifies the job identification number as 100000.  The run simulates 1200 time steps of length 0.3 seconds.  A single frame series file will be collected at time step 1200.  This run uses nonlinear equations and includes bottom friction effects.  The initial wave source will be in the form of surface deformation files.

A total of 4 grids are specified for this simulation.  The first grid is named 2min.  It has a starting latitude of 52 degrees, with the longitude set to 0 degrees (dummy value).  The size of this grid is 870 samples by 300 lines.  The spacing is 120 arc seconds.  The file hsbath_2min.dep contains the bathymetry data and satake_def_2min.def contains the initial deformation information.

The second grid is named 24sec.  It has starting latitude of 55 degrees, with the longitude set to 0 degrees (dummy value).  The grid is 1350 samples by 1050 lines.  It’s spacing is 24 arc seconds.  It is nested into grid 1 in the box bounded by (391,91) to (660,300).  The file hsbath_24sec.dep contains the bathymetry data and file satake_def_24sec_hs.def contains the initial deformation for this grid.

The third grid is named 8sec.  It has starting latitude of 59.254444 degrees, with the longitude set to 0 degrees (dummy value).  The grid is 567 samples by 243 lines.  It’s spacing is 8 arc seconds.  It is nested into grid 2 in the box bounded by (576,639) to (764,719).  The file hsbath_8sec.dep contains the bathymetry data and file satake_def_8sec_hs.def contains the initial deformation for this grid.

The final grid is named hom3sec.  It has starting latitude of 59.5337028503 degrees, with the longitude set to 0 degrees (dummy value).  The grid is 1011 samples by 351 lines.  It has spacing of 2-2/3 arc seconds.  It is nested into grid 3 in the box bounded by (189,127) to (525,243).  The bathymetry data will be read from the file hombath_3sec.dep and the initial deformation information will be read from file satake_def_3sec_hom.def.

The four time series output files created by this run will each contain only a single frame representing the sea level at the 1200th time step.  The four sea level maximum files for this run will contain the maximum sea level observed for each grid during the simulation.  These files will be named:

2min.series				2min.slmax

2min.24sec.series			2min.24sec.slmax

2min.24sec.8sec.series		2min.24sec.8sec.slmax

2min.24sec.8sec.hom3sec.series	2min.24sec.8sec.hom3sec.slmax

A job summary file, named Tsunami.desc, will also be created during post-processing.

################################################################################

# UAF Tsunami Homer input file

################################################################################

########## Global Information ##########

Job_Id=100000

User_Id=logan

Model_Name=UAF_TSUNAMI

Number_of_Time_Steps=1200

Length_Of_Time_Step=.3

Output_Frequency=1200

Global_Nonlinear_Switch=1

Global_Friction_Switch=1

Initial_Wave_Source=FILE

########## Grid Information ###################

Grid_Number=1

Parent=0

Name=2min

Output_Name=2min

Latitude_SW_Corner=52.

Longitude_SW_Corner=0.

East_West_Points=870

North_South_Points=300

Spacing=120

Parent_Child_Spacing_Ratio=0

X_Start=0

X_End=0

Y_Start=0

Y_End=0

Depth_File='hsbath_2min.dep'

Deformation_File='satake_def_2min.def'

######### Grid Information ###################

Grid_Number=2

Parent=1

Name=24sec

Output_Name=2min.24sec

Latitude_SW_Corner=55.

Longitude_SW_Corner=0.

East_West_Points=1350

North_South_Points=1050

Spacing=24

Parent_Child_Spacing_Ratio=5

X_Start=391

X_End=660

Y_Start=91

Y_End=300

Depth_File='hsbath_24sec.dep'

Deformation_File='satake_def_24sec_hs.def'

########## Grid Information ###################

Grid_Number=3

Parent=2

Name=8sec

Output_Name=2min.24sec.8sec

Latitude_SW_Corner=59.254444

Longitude_SW_Corner=0.

East_West_Points=567

North_South_Points=243

Spacing=8

Parent_Child_Spacing_Ratio=3

X_Start=576

X_End=764

Y_Start=639

Y_End=719

Depth_File='hsbath_8sec.dep'

Deformation_File='satake_def_8sec_hs.def'

########### Grid Information ###################

Grid_Number=4

Parent=3

Name=hom3sec

Output_Name=2min.24sec.8sec.hom3sec

Latitude_SW_Corner=59.5337028503

Longitude_SW_Corner=0.

East_West_Points=1011

North_South_Points=351

Spacing=2.6666666667

Parent_Child_Spacing_Ratio=3

X_Start=189

X_End=525

Y_Start=127

Y_End=243

Depth_File='hombath_3sec.dep'

Deformation_File='satake_def_3sec_hom.def'

# APPENDIX B: Example Comcot.cfg configuration File

This appendix contains an example Comcot.cfg file.

The general parameters specify the job identification number as 200000.  This run is 2700 time steps in length with each step in the outermost grid being 2 seconds in duration (for a total simulated time of 1 hour 30 minutes).  This control files specifies a run with 3 layers (grids).  Since the time step for the outermost grid will be 2 seconds, it will be 1 second for the 2nd layer, and 0.5 seconds for the 3rd layer.

Time series output will be written every 150 time steps (simulating 5 minutes of propagation) for a total of 18 frames.  This run uses 0.013 for the relative roughness coefficient.  The initial wave source will be in the form of a surface deformation file.

The first grid, named layer1, has a southern boundary latitude of 21.5 degrees, with a dummy longitude value of 0 degrees. The size of the grid is 100 lines by 100 samples.  The grid length (spacing) is 60 arc seconds. This layer uses spherical coordinates with a linear governing equation that neglects bottom friction.  The input topo/bathy file is named layer1.dep and the initial surface deformation file named ini_surface.def

The second grid, named layer2, has a southern boundary latitude of 22.33 degrees, with a dummy longitude value of 0 degrees. The size of the grid is 106 lines by 106 samples.  The grid spacing is 20 arc seconds.  It is nested into grid 1 in the box bounded by (21,51) to (55,85).  Layer2 uses spherical coordinates with a linear governing equation that neglects bottom friction.  The input topo/bathy file named layer2.dep will be used for this grid.

The third grid, named layer3, has a southern boundary latitude of 22.457 degrees, with a dummy longitude value of 0 degrees. The size of the grid is 181 lines by 181 samples.  The grid spacing is 6-2/3 arc seconds. It is nested into grid 2 in the box bounded by (23,23) to (82,82).  Layer3 uses spherical coordinates with a linear governing equation that neglects bottom friction.  The input topo/bathy file named layer3.dep will be used for this grid.

Each of the three time series files created by this run will contain 18 frames representing the sea level every 150 time steps.  The three sea level maximum files will contain the maximum sea level observed for each grid during the simulation.  These files will be named:

layer1.series				layer1.slmax

layer1.layer2.series			layer1.layer2.slmax

layer1.layer2.layer3.series		layer1.layer2.layer3.slmax

A job summary file, named Comcot.desc, will also be created during the post-processing steps at ARSC.

################################################################################

# Configuration file for COMCOT program

################################################################################

########## Global Information ##########

Job_Id=200000

User_Id=logan

Model_Name=COMCOT

Number_of_Time_Steps=2700

Length_Of_Time_Step=2.0

Output_Frequency=150

Coef_of_Bottom_Friction=0.013

Initial_Wave_Source=FILE

########## Grid Information ###################

Grid_Number=1

Parent=0

Name=layer1

Output_Name=layer1

Latitude_SW_Corner=21.5

Longitude_SW_Corner=0.

East_West_Points=100

North_South_Points=100

Spacing=60

Parent_Child_Spacing_Ratio=0

X_Start=0

X_End=0

Y_Start=0

Y_End=0

Coordinate_Switch=0

Nonlinear_Switch=0

Friction_Switch=0

Depth_File='layer1.dep'

Deformation_File='ini_surface.dat'

Grid_Number=2

Parent=1

Name=layer2

Output_Name=layer1.layer2

Latitude_SW_Corner=22.33

Longitude_SW_Corner=0.

East_West_Points=105

North_South_Points=105

Spacing=20

Parent_Child_Spacing_Ratio=3

X_Start=21

X_End=55

Y_Start=51

Y_End=85

Coordinate_Switch=0

Nonlinear_Switch=0

Friction_Switch=0

Depth_File='layer2.dep'

Grid_Number=3

Parent=2

Name=layer3

Output_Name=layer1.layer2.layer3

Latitude_SW_Corner=22.457

Longitude_SW_Corner=0.

East_West_Points=180

North_South_Points=180

Spacing=6.666666667

Parent_Child_Spacing_Ratio=3

X_Start=23

X_End=82

Y_Start=23

Y_End=82

Coordinate_Switch=0

Nonlinear_Switch=0

Friction_Switch=0

Depth_File='layer3.dep

# APPENDIX C: Example Tsunami_CLAW.cfg configuration file

This appendix contains an example Tsunami_CLAW.cfg configuration file.

The general parameters specify a job identification number of 300000.  This run will simulate a total of 5400 seconds (1 hour 30 minutes).  The length of the time steps and the total number of time steps executed by the model is variable and is not controlled by these parameters.

Time series output will be written a total of 18 times during the run at equal intervals (simulating 5 minutes of propagation).  The run uses bottom friction with a value of 0.025 for the coefficient of friction.  The initial wave source will be in the form of a surface deformation file.

Over the entire domain of calculation, a maximum refinement level of 4 will be allowed.  The adaptive mesh will be flagged for refinement every time step of the simulation.  Any depth less than 1000 meters will be considered shallow water and eligible for refinement.  Any surface height over 0.01 meters will be considered a valid moving wave and may be flagged for refinement.  The topmost layer of the simulation will have only 12 east-west cells and 12 north-south cells.

The first grid, named layer1, has a southern boundary latitude of 21.5 degrees, with a dummy longitude value of 0 degrees.  The northern boundary latitude is 23.1666667 degrees, with a (dummy) longitude of 1.6666667 degrees. The size of the grid is 100 lines by 100 samples.  The grid length (spacing) is 60 arc seconds. This layer uses spherical coordinates.  The input topo/bathy file is named layer1.dep and the initial surface deformation file named ini_surface.def.  In this grid, a maximum refinement level of 2 is allowed.

The second grid, named layer2, has a southern boundary latitude of 22.33 degrees, with a dummy longitude value of 0 degrees.  The northern latitude is 22.91333333 degrees, with a (dummy) longitude of 0.58333333.  The size of the grid is 105 lines by 105 samples.  The grid spacing is 20 arc seconds. Layer2 also uses spherical coordinates.  The input topo/bathy file named layer2.dep will be used for this grid.  A maximum refinement level of 3 is allowed in this grid.

The third grid, named layer3, has a southern boundary latitude of 22.457 degrees, with a dummy longitude value of 0 degrees. The northern latitude is 22.79033333 degrees, with a (dummy) longitude of 0.33333333.  The size of the grid is 180 lines by 180 samples.  The grid spacing is 6-2/3 arc seconds. Layer3 uses spherical coordinates. The input topo/bathy file named layer3.dep will be used for this grid.  A maximum refinement level of 4 is allowed in this grid.

A job summary file, named Tsunami_CLAW.desc, will also be created during the post-processing steps at ARSC.

################################################################################

# Configuration file for Tsunami CLAW program

################################################################################

########## Global Information ##########

Job_Id=300000

User_Id=logan

Model_Name=TSUNAMI_CLAW

End_Time=5400

Number_of_Outputs=18

Global_Friction_Switch=1

Coef_of_Bottom_Friction=0.025

Initial_Wave_Source=FILE

Global_Max_Refinement=4

Refinement_Frequency=1

Shallow_Depth=1000.0

Wave_Tolerance=0.01

East_West_Cells=12

North_South_Cells=12

########## Grid Information ###################

Grid_Number=1

Name=layer1

Output_Name=layer1

Latitude_SW_Corner=21.5

Longitude_SW_Corner=0.

Latitude_NE_Corner=23.16666667

Longitude_NE_Corner=1.6666667

East_West_Points=100

North_South_Points=100

Spacing=60

Parent_Child_Spacing_Ratio=0

Coordinate_Switch=0

Depth_File='layer1.dep'

Deformation_File='ini_surface.dat'

Bathy_Max_Refinement=2

Grid_Number=2

Name=layer2

Output_Name=layer1.layer2

Latitude_SW_Corner=22.33

Longitude_SW_Corner=0.

Latitude_NE_Corner=22.91333333

Longitude_NE_Corner=0.58333333

East_West_Points=105

North_South_Points=105

Spacing=20

Parent_Child_Spacing_Ratio=3

Coordinate_Switch=0

Depth_File='layer2.dep'

Bathy_Max_Refinement=3

Grid_Number=3

Name=layer3

Output_Name=layer1.layer2.layer3

Latitude_SW_Corner=22.457

Longitude_SW_Corner=0.

Latitude_NE_Corner=22.79033333

Longitude_NE_Corner=0.33333333

East_West_Points=180

North_South_Points=180

Spacing=6.666666667

Parent_Child_Spacing_Ratio=3

Coordinate_Switch=0

Depth_File='layer3.dep

Bathy_Max_Refinement=4

# APPENDIX D: Additional Parameters for UAF Tsunami

# Configuration Parameters

## General Parameters

### Display_Frequency

Definition: The frequency with which progress statements are displayed during a run.  This parameter is most useful for an interactive run or debugging purposes.

Required: Optional.  If not specified, progress statements are displayed every 100 time steps.

Type: INT

Units: Time Steps

Range: 1 to Number of Time Steps

Default: 100

### Watch_Frequency

Definition: The frequency of output to the watch point and watch line files.

Required: Optional.  If not specified, output will be generated every 100 time steps.

Type: INT

Units: Time Steps

Range: 1 to Number of Time Steps

Default: 100

Notes: The occurrence of watchpoints and watchlines are independent.  Zero or more watchpoints may occur in zero or more grids.  Similarly, zero or more watchlines may occur in zero or more grids.  Only one grid has to have a watchpoint or watchline in order for this parameter to be utilized.  Note this parameter is truly optional since specification of a watchline/point will use the default of 100 if Watch_Frequency does not appear in the configuration file.

### Constant_Depth

Definition: Switch to set bathymetry as a constant depth of 200 meters.

Required: Optional.  Never required.  This is used to simulate waves under controlled laboratory conditions, such as in a wave flume or basin.

Type: BIN

Range: 0 – Not constant depth; 1 – Use constant depth

Default: Not constant depth

Notes:  If Constant_Depth=1, no bathymetry files will be read.

### Input_Format

Definition: Switch to determine the format of bathymetry and initial surface deformation input files.

Required: Optional.  If not specified, input files are assumed to be BINARY.

Type: STRING

Range: ASCII | BINARY

Default: BINARY

Notes: Currently, the bathymetry and initial surface displacement input files have to be in the same format, either ASCII or BINARY.  Different formats for the two are not allowed. However, hopefully this won’t be a problem - when we allow users to supply initial surface files, the portal front-end will have to provide a mechanism to ‘upload’ the files from the user to be included into a run.  It would make sense to ingest them into the database (in binary format) and then include them in the portal job.  If this does not prove to be feasible, the codes can be modified to have Input_Deformation_Format and Input_Bathymetry_Format (maybe this is the better solution anyhow?)

### Output_Format

Definition: Switch to determine the format of sea level series and sea level maximum output files.

Required: Optional.  If not specified, output file be in BINARY format.

Type: STRING

Range: ASCII | BINARY

Default: BINARY

Notes: This switch simply determines the format of the output, either ASCII or BINARY.  Thus, it is truly optional.  If it does not appear, BINARY is assumed.

### Save_Maximum

Definition: Switch to determine is sea level maximums will be reported.

Required: Optional.  Never required

Type: BIN

Range: 0 – Do not track or report sea level maximums; 1 – create slmax files

Default: 1 – create slmax files

Notes:  If Save_Maximum=0, no sea level maximum (slmax) files will be created.

### Save_Minimum

Definition: Switch to determine is sea level minimums will be reported.

Required: Optional.  Never required

Type: BIN

Range: 0 – Do not track or report sea level minimums; 1 – create slmin files

Default: 0 – do not create slmin files

Notes:  If Save_Minimum=1, a sea level minimum (slmin) files will be created.  They are all in respects, save file name (.slmin) and meaning (minimum), the same format as there corresponding slmax counterparts.

## Grid Specific Watch Point Parameters

### Watch_Point

Definition: Defines a grid point as a “watch point”, wherein a time series of selected physical values will be collected.

Required: Optional.  If present, values must also be specified for the following:  Watch_Frequency, WP_j, WP_k, WP_Param

Type: Integer

Units: NA

Range: 1 .. 100

Default: 1, 2, 3, … (sequentially numbered from 1)

### WP_j

Definition: j index of watch point

Required: Optional.  Required if a Watch_Point is specified (i.e., based upon occurrence of Watch_Point parameter)

Type: Integer

Units: Points

### WP_k

Definition: k index of watch point

Required: Optional.    Required if a Watch_Point is specified (i.e., based upon occurrence of Watch_Point parameter)

Type: Integer

Units: Points

### WP_Param

Definition: Defines which parameter to watch at this point.  Values in the time series can come from either U-velocity, V-velocity, sea level, or normal velocity, based upon the value of this parameter.

Required: Optional.    Required if a Watch_Point is specified (i.e., based upon occurrence of Watch_Point parameter)

Type: STRING

Range: UVEL | VVEL | SEA_LEVEL | VELNORM

Default: NA

## Grid Specific Watch Line Parameters

For the grid specific watch lines, values are stored according to the following algorithm at the frequency specified by the Watch_Frequency parameter:

j=Start_j; k=Start_k

do h=1,Line_Length

stored_values(h) = SeaLevel(j,k)

if (Line_Direction==1) then      		! Horizontal line

j=j+Line_Sign

else if (Line_Direction==-1) then  	! Vertical line

k=k+Line_Sign

end if

end do

### Watch_Line

Definition: Defines a line in a grid as a “watch line”, wherein a time series of selected sea levels will be collected.

Required: Optional.  If present, values must also be specified for the following:  Watch_Frequency, Start_j, Start_k, Line_Length, Line_Direction, and Line_Size

Type: STRING

Notes: The value given to the Watch_Line parameter is a user definable string that will be the watch line output file name.

### Start_j

Definition: Starting J-coordinate for watch line

Required: Optional.  Required if a Watch_Line is specified (i.e., based upon occurrence of Watch_Line parameter)

Type: Integer

Units: Grid points

Range: 1 .. East_West_Points

Default: NA

Granularity: 1

### Start_k

Definition: Starting K-coordinate for watch line

Required: Optional.  Required if a Watch_Line is specified (i.e., based upon occurrence of Watch_Line parameter)

Type: Integer

Units: Grid points

Range: 1 .. North_South_Points

Default: NA

Granularity: 1

### Line_Length

Definition: Length of the watch line

Required: Optional.  Required if a Watch_Line is specified (i.e., based upon occurrence of Watch_Line parameter)

Type: Integer

Units: Grid points

Range: The maximum value for this parameter should be based upon the Line_Direction, Line_Sign, Start_j, Start_k, East_West_Points, and North_South_Points for this grid according to the following table:

| Line_Direction | Line_Sign | Maximum Line_Length |
| --- | --- | --- |
| 1 | -1 | Start_j |
| 1 | 1 | East_West_Points-Start_j |
| -1 | -1 | Start_k |
| -1 | 1 | North_South_Points-Start_k |

Default:  NA

Granularity: 1

### Line_Direction

Definition: Defines the direction of this watch line, either horizontal (1) or vertical (-1)

Required: Optional Required if a Watch_Line is specified (i.e., based upon occurrence of Watch_Line parameter)

Type: Integer

Units: NA

Range: -1 or 1

Default: NA

Granularity: NA

Notes:  The direction of the watch line is determined by this parameter.  If it is 1, the line will be horizontal.  If it is -1, the line will be vertical.

### Line_Sign

Definition: Defines the direction of this watch line, either positive from the starting point (1) or negative from the starting point (-1).

Required: Optional.  Required if a Watch_Line is specified (i.e., based upon occurrence of Watch_Line parameter)

Type: Integer

Units: NA

Range: -1 or 1

Default: NA

Granularity: NA

# Parameters for Initial Conditions

Beyond fault generation, two additional initial conditions can be used for UAF Tsunami.  The first is to read initial surface deformation from files.  However, if the parameters in section 2.2 below are defined in the configuration file, a sine wave can be introduced into the simulation instead.

## File Configuration Parameters

By default, the grid specific parameter Deformation_File gives the name of the input deformation file.  This one instance of this parameter must exist in the configuration file for each grid defined.

## Sine Wave Configuration Parameters

When the Initial_Wave_Source=WAVE is defined, the additional parameters listed in table 6 are needed to describe the wave being introduced.

| PARAMETER KEYWORD | TYPE | UNITS |
| --- | --- | --- |
| Sin_Wave_j1 | INT | Points |
| Sin_Wave_j2 | INT | Points |
| Sin_Wave_k1 | INT | Points |
| Sin_Wave_k2 | INT | Points |
| Sin_Wave_Amp | REAL | cm |
| Sin_Wave_Period | REAL | sec |

Table 6:  Summary of Sine Wave Generation Parameters

### Sin_Wave_j1

Definition: j index of first point

Required: Optional based upon Sin_Wave_Deformation

Type: INT

### Sin_Wave_j2

Definition: j index of second point

Required: Optional based upon Sin_Wave_Deformation

Type: INT

### Sin_Wave_k1

Definition: k index of first point

Required: Optional based upon Sin_Wave_Deformation

Type: INT

### Sin_Wave_k2

Definition: k index of second point

Required: Optional based upon Sin_Wave_Deformation

Type: INT

### Sin_Wave_Amp

Definition: Amplitude of sine wave

Required: Optional based upon Sin_Wave_Deformation

Type: REAL

Units: centimeters

Default: 200 cm

### Sin_Wave_Period

Definition: Period of sine wave.

Required: Optional based upon Sin_Wave_Deformation

Type: REAL

Units: seconds

Default: 600

# APPENDIX E: Additional Parameters for COMCOT

# General Parameters

## Input_Format

Definition: Switch to determine the format of bathymetry and initial surface displacement input files.

Required: Optional.

Type: STRING

Range: ASCII | BINARY

Default: BINARY

Notes: Currently, the bathymetry and initial surface displacement input files have to be in the same format, either ASCII or BINARY.  Different formats for the two are not allowed. However, hopefully this won’t be a problem - when we allow users to supply initial surface files, the portal front-end will have to provide a mechanism to ‘upload’ the files from the user to be included into a run.  It would make sense to ingest them into the database (in binary format) and then include them in the portal job.  If this does not prove to be feasible, the codes can be modified to have Input_Deformation_Format and Input_Bathymetry_Format (maybe this is the better solution anyhow?)

## Output_Format

Definition: Switch to determine the format of sea level series, sea level max, and initial surface displacement output files.

Required: Optional.  Required when user wants output files to be ASCII rather than binary format.

Type: STRING

Range: ASCII | BINARY

Default: BINARY

## Save_Maximum

Definition: Switch to determine is sea level maximums will be reported.

Required: Optional, if this parameter is not specified slmax files will be created.

Type: BIN

Range: 0 – Do not track or report sea level maximums; 1 – create slmax files

Default: 1 – create slmax files

Notes:  If Save_Maximum=0, no sea level maximum (slmax) files will be created.

Asserting Save_Maximum=1 is the same as not providing the parameter at all.

## Save_Minimum

Definition: Switch to determine is sea level minimums will be reported.

Required: Optional, if this parameter is not specified slmin files will not be created.

Type: BIN

Range: 0 – Do not track or report sea level minimums; 1 – create slmin files

Default: 0 – do not create slmin files

Notes:  If Save_Minimum=1, sea level minimum (slmin) files will be created.  They are all in respects, save file name (.slmin) and meaning (minimum rather than maximum), the same format as there corresponding slmax counterparts. Asserting Save_Minimum=0 is the same as not providing the parameter at all.

# General Parameters for Initial Conditions

## File Configuration Parameters

When the value of FILE is used for the Initial_Wave_Source, the grid specific parameter Deformation_File must exist in the configuration file for the first grid.

## Wave Configuration Parameters

When the value of WAVE is used, additional parameters have to be defined to describe the wave being introduced.  Based upon the wave type and incident direction selected, a variety of the parameters listed in table 7 will have to be defined.

| TYPE | PARAMETER KEYWORD | TYPE | UNITS | NOTES |
| --- | --- | --- | --- | --- |
| WAVE | Wave_Type | INT | 0-2 | 0-Sine; 1-Solitary; 2-Given Form |
|  | Wave_Incident_Direction | INT | 1-5 | 1:top, 2:bt, 3:lf, 4:rt, 5:ob |
|  | Wave_Time_To_Change_Boundary | REAL | Seconds |  |
|  | Wave_Boundary_After_Wave | BIN | 0,1 | 0:open, 1:solid |
|  | Wave_Angular_Frequency | REAL | W |  |
|  | Wave_Height | REAL | Meters |  |
|  | Wave_Depth | REAL | Meters |  |
|  | Oblique_i_Index | INT | Points | Needed if Incident is Oblique |
|  | Oblique_j_Index | INT | Points | Needed if Incident is Oblique |
|  | Oblique_Angle | REAL | Degrees | Needed if Incident is Oblique |
|  | Profile_Name | FILE |  | Needed if Type is Given Form |
|  | Profile_Length | INT |  | Needed if Type is Given Form |

Table 7:  Summary of Wave Generation Parameters

### Wave_Type

Definition: Type of wave to introduce.

Required: Optional.  Required when Initial Wave Source is set to WAVE

Type: INT

Range: 0 – Sine; 1- Solitary; 2 – Given form

Default: None

Notes:  Parameters required for each option are summarized in table 8.  Since all three wave types allow selection of an incident direction, the oblique parameters (2.2.8-2.2.10) may be combined with any of the wave types.

| Option | Parameters |
| --- | --- |
| 0 | 2.2.2-2.2.7 [2.2.8-2.2.10] |
| 1 | 2.2.2, 2.2.6, 2.2.7, [2.2.8-2.2.10] |
| 2 | 2.2.2-2.2.4, 2.2.7, 2.2.11-2.2.12 [2.2.8-2.2.10] |

Table 8:  Parameters required by different Wave_Type options

### Wave_Incident_Direction

Definition:  Specifies incident direction of incoming wave.  Valid values are:

1: waves come from top boundary of the domain;

2: waves come from bottom boundary of the domain;

3: waves come from left boundary of the domain;

4: waves come from right boundary of the domain;

5: Oblique incident wave.

Required: Optional.  Required when Initial Wave Source is set to WAVE.  Specifying either 2 or 5 requires additional parameters (see Notes)

Type: INT

Range: 1-5

Default: NA

Notes:  When option 5 is chosen, the oblique parameters (Oblique_i_Index, Oblique_j_Index, and Oblique_Angle, described in 2.2.8-2.2.10) must be defined.  These parameters define the i,j index of a point and an angle.  Waves will generate from a straight line through the point with the slope defined by the angle.  The angle is measured counterclockwise from the rightward direction.  When option 2 is chosen, the profile parameters (Profile_Name and Profile_Length, described in 2.2.11-2.2.12) must be defined.  These define a file that specifies the form of the wave, in ASCII format.

### Wave_Time_to_Change_Boundary

Definition: Time to stop sending in wave.

Required: Optional.  Required when Initial Wave Source is set to WAVE

Type: REAL

Units: Seconds

### Wave_Boundary_After_Wave

Definition: Boundary conditions after the wave stops.

Required: Optional.  Required when Initial Wave Source is set to WAVE

Type: BIN

Range: 0 – open boundary 1- solid (closed) boundary

Default: NA

### Wave_Angular_Frequency

Definition: Angular frequency of generated wave.

Required: Optional.  Required when Initial Wave Source is set to WAVE

Type: REAL

Units: w

### Wave_Height

Definition: Height of generated wave.

Required: Optional.  Required when Initial Wave Source is set to WAVE

Type: REAL

Units: Meters

### Wave_Depth

Definition: Depth of water wave is generated in.

Required: Optional.  Required when Initial Wave Source is set to WAVE

Type: REAL

Units: Meters

### Oblique_i_Index

Definition: I index of oblique point

Required: Optional.  Required when Initial Wave Source is set to WAVE and Wave_Incident_Direction is 5 (oblique incident wave)

Type: INT

Units: Points

### Oblique_j_Index

Definition: J index of oblique point

Required: Optional.  Required when Initial Wave Source is set to WAVE and Wave_Incident_Direction is 5 (oblique incident wave)

Type: INT

Units: Points

### Oblique_Angle

Definition:

Required: Optional.  Required when Initial Wave Source is set to WAVE and Wave_Incident_Direction is 5 (oblique incident wave)

Type: REAL

### Profile_Name

Definition: Name of the file containing the given form for the wave.

Required: Optional.  Required when Initial Wave Source is set to WAVE and Wave_Incident_Direction is 2 (waves from bottom boundary)

Type: FILE

Default: fse2.dat

Notes:  The given form file contains a series of time (sec), wave height (meter) pairs of values in ASCII format.  This is the only file that does NOT obey the Input_Format parameter – it is always assumed to be in ASCII format; never in binary format.  The given time series is introduced into the simulation using the selected incident direction.

### Profile_Length

Definition: Number of samples in the given form file.

Required: Optional.  Required when Initial Wave Source is set to WAVE and Wave_Incident_Direction is 2 (waves from bottom boundary)

Type: INT

Range: maximum 1000